## Slide 1: Project Morpheus: Supersonic Transport Jet Design
Charles Evans, Grace Krahn, Alec Liberman, Juan Jose Paez, and Eric Qiu
11 April 2022

## Slide 2: Mission Overview
RFP: design a supersonic transport aircraft to carry out two possible missions
Standard mission: normal mission with supersonic cruise
Alternate mission: takeoff, subsonic cruise, supersonic cruise, subsonic cruise, descent and landing

## Slide 3: Requirements
Payload: 50 passengers with baggage & 4 crew
Engines: 4 low-bypass turbofan engines
Range: 4000 nm supersonic cruise or 1000 nm subsonic cruise and 3000 nm supersonic cruise
  Supersonic cruise at Mach 2 at 55000 ft
  Subsonic cruise at Mach 0.95 at 35000 ft
Approach speed: 140 knots
Runway length: 8500 ft

## Slide 4: Mission Profile
Standard mission
  4000 nm Mach 2 cruise
Alternate mission
  3000 nm Mach 2 cruise
  Two 500 nm subsonic segments
  Requirement pushback on subsonic cruise altitude (< 50,000 ft)
  Sizing mission

## Slide 5: Market Analysis
Renewed interest in SST aircraft due to gap left by Concorde and Tu-144
Engine performance, aerodynamic understanding, other improvements lead to higher efficiency than late 20th-century design allowed
Supersonic jet market size in North America alone
  2019: $8.87 bil USD
  2020: $8.93 bil USD
  2030: $35.62 bil USD (projected)
Virgin Group, Japan Airlines, others have garnered $6 bil worth of pre-orders for similar aircraft
Project Morpheus fills the trans-Atlantic business travel niche

## Slide 6: Configuration Selection
Weighted Pugh matrices evaluated component configuration options using the FOM:
  Wing shape: highly swept with Yehudi, ogival delta, double delta, trapezoidal with canard
  Engine location: below wing, above and below wing, tail-mounted
  Tail type: T-tail, conventional, split V-tail, single vertical tail
  Fuselage: standard, blended wing, wide
  Landing gear layout: trike, tail dragger, tandem
Figure of Merit (FOM) | Relative Weight | Definition
Stability | 0.1 | Relative contributions of features to overall aircraft stability
Controls scheme | 0.1 | Optimality of control surface locations, sizes, & interconnectedness
Development cost | 0.1 | Upfront cost needed to achieve technology and design readiness
Maintainability | 0.3 | Comparative upkeep cost in the system complexity and accessibility
Manufacturing simplicity | 0.1 | Relative ease of creating and mechanically assembling the system
Supersonic performance | 0.3 | Assessment of aerodynamic qualities (drag) at supersonic cruise
*Note: bolded words are the chosen configuration

## Slide 7: Design Overview
130 ft
6 ft
48 ft
59 ft
21 ft
6.2 ft
75°
48°
Passengers: 50
Engines: 4
Wing area: 1180 ft2
Aspect ratio: 1.95

## Slide 8: Aircraft Size Comparison
Aircraft | Length
Project Morpheus | 130'
Concorde | 203'
Boom Overture | 205'
QueSST X-Plane | 94'
Tupolev Tu-144 | 216'
https://www.pinterest.com/pin/344666177708740775/
https://boomsupersonic.com/overture
https://fineartamerica.com/featured/2-british-airways-concorde-1997-to-2003-steve-h-clark-photography.html
https://www.kclu.org/local-news/2022-02-10/south-coast-based-aviation-historian-authors-new-book-about-history-of-groundbreaking-x-plane-series
Supersonic Cruise Aircraft Lengths

## Slide 9: Vehicle Weights
Aircraft | MGTOW (lb) | Empty Weight (lb) | Max # of Passengers
Concorde | 408,000 | 173,500 | 100
Boom Overture | 265,600 | 218,700 | 88
QueSST X-Plane | 25,000 | 14,990 | 1
Tupolev Tu-144 | 456,357 | 218,699 | 135
Boeing 737 MAX 7 | 177,000 | 138,700 | 153
Weight | Value (lb)
MGTOW | 129,815
Empty | 58,346
Fuel | 58,590
Payload | 11,500
Weight Comparison to Other Aircraft
Project Morpheus Weights

## Slide 10: Constraint Sizing
Weights
  MGTOW
  Empty
  Fuel
  Payload
Comparison to existing aircraft weights
Chart: Thrust-to-Weight Ratio (~) vs. Wing Loading (psf), All Performance Constraints
| 50 | 52.5 | 55 | 57.5 | 60 | 62.5 | 65 | 67.5 | 70 | 72.5 | 75 | 77.5 | 80 | 82.5 | 85 | 87.5 | 90 | 92.5 | 95 | 97.5 | 100 | 102.5 | 105 | 107.5 | 110 | 112.5 | 115 | 117.5 | 120 | 122.5 | 125 | 127.5 | 130 | 132.5 | 135 | 137.5 | 140 | 142.5 | 145 | 147.5 | 150
1 - Standard Cruise | 0.66145 | 0.63571 | 0.61258 | 0.59172 | 0.57284 | 0.55571 | 0.54012 | 0.52591 | 0.51292 | 0.50103 | 0.49013 | 0.48012 | 0.47093 | 0.46247 | 0.45468 | 0.4475 | 0.44089 | 0.43479 | 0.42917 | 0.42399 | 0.41922 | 0.41482 | 0.41077 | 0.40705 | 0.40363 | 0.4005 | 0.39763 | 0.395 | 0.39261 | 0.39044 | 0.38847 | 0.38669 | 0.3851 | 0.38368 | 0.38242 | 0.38131 | 0.38035 | 0.37952 | 0.37883 | 0.37826 | 0.3778
2 - Alternate Cruise | 0.6426 | 0.61707 | 0.5941 | 0.57336 | 0.55455 | 0.53746 | 0.52189 | 0.50766 | 0.49463 | 0.48268 | 0.4717 | 0.4616 | 0.45229 | 0.4437 | 0.43577 | 0.42844 | 0.42166 | 0.41539 | 0.40959 | 0.40422 | 0.39924 | 0.39464 | 0.39038 | 0.38643 | 0.38279 | 0.37942 | 0.37631 | 0.37344 | 0.37081 | 0.36838 | 0.36616 | 0.36412 | 0.36227 | 0.36058 | 0.35905 | 0.35767 | 0.35643 | 0.35533 | 0.35436 | 0.3535 | 0.35276
3 - Slow Cruise 1 | 0.34324 | 0.33588 | 0.32962 | 0.3243 | 0.3198 | 0.31604 | 0.31291 | 0.31036 | 0.30833 | 0.30674 | 0.30558 | 0.30478 | 0.30432 | 0.30417 | 0.3043 | 0.30468 | 0.3053 | 0.30614 | 0.30717 | 0.30839 | 0.30977 | 0.31131 | 0.313 | 0.31483 | 0.31678 | 0.31885 | 0.32102 | 0.32331 | 0.32568 | 0.32815 | 0.33071 | 0.33334 | 0.33606 | 0.33884 | 0.34169 | 0.3446 | 0.34758 | 0.35061 | 0.35369 | 0.35683 | 0.36002
4 - Slow Cruise 2 | 0.30277 | 0.29339 | 0.2851 | 0.27776 | 0.27124 | 0.26545 | 0.26031 | 0.25573 | 0.25167 | 0.24807 | 0.24488 | 0.24206 | 0.23958 | 0.2374 | 0.23551 | 0.23387 | 0.23246 | 0.23128 | 0.23028 | 0.22948 | 0.22884 | 0.22836 | 0.22802 | 0.22782 | 0.22775 | 0.2278 | 0.22795 | 0.22821 | 0.22857 | 0.22901 | 0.22954 | 0.23016 | 0.23084 | 0.2316 | 0.23243 | 0.23332 | 0.23427 | 0.23528 | 0.23634 | 0.23746 | 0.23862
5 - Climb | 0.43338 | 0.42245 | 0.41275 | 0.40411 | 0.39641 | 0.38952 | 0.38337 | 0.37786 | 0.37293 | 0.36851 | 0.36456 | 0.36103 | 0.35788 | 0.35507 | 0.35258 | 0.35038 | 0.34845 | 0.34676 | 0.34529 | 0.34403 | 0.34296 | 0.34206 | 0.34134 | 0.34076 | 0.34033 | 0.34003 | 0.33985 | 0.33979 | 0.33984 | 0.34 | 0.34024 | 0.34058 | 0.34101 | 0.34152 | 0.3421 | 0.34275 | 0.34347 | 0.34426 | 0.34511 | 0.34602 | 0.34698
6 - Takeoff | 0.17882 | 0.18776 | 0.1967 | 0.20564 | 0.21458 | 0.22352 | 0.23246 | 0.2414 | 0.25034 | 0.25928 | 0.26822 | 0.27717 | 0.28611 | 0.29505 | 0.30399 | 0.31293 | 0.32187 | 0.33081 | 0.33975 | 0.34869 | 0.35763 | 0.36657 | 0.37551 | 0.38446 | 0.3934 | 0.40234 | 0.41128 | 0.42022 | 0.42916 | 0.4381 | 0.44704 | 0.45598 | 0.46492 | 0.47386 | 0.4828 | 0.49175 | 0.50069 | 0.50963 | 0.51857 | 0.52751 | 0.53645
7- Approach | 0 | 0.125 | 0.25 | 0.375 | 0.5
Design Point | 0.405
T/W (~) | W/S (psf)
0.405 | 111.6
Project Morpheus
T/W (~) | W/S (psf)
0.373 | 106.8
Concorde
Aircraft | T/W (~) | W/S (psf)
Project Morpheus | 0.405 | 111.6
Concorde | 0.373 | 106.8
Tupolev Tu-144 | 0.440 | 83.7
Chart: Thrust-to-Weight Ratio (~) vs. Wing Loading (psf), All Performance Constraints
| 50 | 52.5 | 55 | 57.5 | 60 | 62.5 | 65 | 67.5 | 70 | 72.5 | 75 | 77.5 | 80 | 82.5 | 85 | 87.5 | 90 | 92.5 | 95 | 97.5 | 100 | 102.5 | 105 | 107.5 | 110 | 112.5 | 115 | 117.5 | 120 | 122.5 | 125 | 127.5 | 130 | 132.5 | 135 | 137.5 | 140 | 142.5 | 145 | 147.5 | 150
1 - Standard Cruise | 0.66145 | 0.63571 | 0.61258 | 0.59172 | 0.57284 | 0.55571 | 0.54012 | 0.52591 | 0.51292 | 0.50103 | 0.49013 | 0.48012 | 0.47093 | 0.46247 | 0.45468 | 0.4475 | 0.44089 | 0.43479 | 0.42917 | 0.42399 | 0.41922 | 0.41482 | 0.41077 | 0.40705 | 0.40363 | 0.4005 | 0.39763 | 0.395 | 0.39261 | 0.39044 | 0.38847 | 0.38669 | 0.3851 | 0.38368 | 0.38242 | 0.38131 | 0.38035 | 0.37952 | 0.37883 | 0.37826 | 0.3778
2 - Alternate Cruise | 0.6426 | 0.61707 | 0.5941 | 0.57336 | 0.55455 | 0.53746 | 0.52189 | 0.50766 | 0.49463 | 0.48268 | 0.4717 | 0.4616 | 0.45229 | 0.4437 | 0.43577 | 0.42844 | 0.42166 | 0.41539 | 0.40959 | 0.40422 | 0.39924 | 0.39464 | 0.39038 | 0.38643 | 0.38279 | 0.37942 | 0.37631 | 0.37344 | 0.37081 | 0.36838 | 0.36616 | 0.36412 | 0.36227 | 0.36058 | 0.35905 | 0.35767 | 0.35643 | 0.35533 | 0.35436 | 0.3535 | 0.35276
3 - Slow Cruise 1 | 0.34324 | 0.33588 | 0.32962 | 0.3243 | 0.3198 | 0.31604 | 0.31291 | 0.31036 | 0.30833 | 0.30674 | 0.30558 | 0.30478 | 0.30432 | 0.30417 | 0.3043 | 0.30468 | 0.3053 | 0.30614 | 0.30717 | 0.30839 | 0.30977 | 0.31131 | 0.313 | 0.31483 | 0.31678 | 0.31885 | 0.32102 | 0.32331 | 0.32568 | 0.32815 | 0.33071 | 0.33334 | 0.33606 | 0.33884 | 0.34169 | 0.3446 | 0.34758 | 0.35061 | 0.35369 | 0.35683 | 0.36002
4 - Slow Cruise 2 | 0.30277 | 0.29339 | 0.2851 | 0.27776 | 0.27124 | 0.26545 | 0.26031 | 0.25573 | 0.25167 | 0.24807 | 0.24488 | 0.24206 | 0.23958 | 0.2374 | 0.23551 | 0.23387 | 0.23246 | 0.23128 | 0.23028 | 0.22948 | 0.22884 | 0.22836 | 0.22802 | 0.22782 | 0.22775 | 0.2278 | 0.22795 | 0.22821 | 0.22857 | 0.22901 | 0.22954 | 0.23016 | 0.23084 | 0.2316 | 0.23243 | 0.23332 | 0.23427 | 0.23528 | 0.23634 | 0.23746 | 0.23862
5 - Climb | 0.43338 | 0.42245 | 0.41275 | 0.40411 | 0.39641 | 0.38952 | 0.38337 | 0.37786 | 0.37293 | 0.36851 | 0.36456 | 0.36103 | 0.35788 | 0.35507 | 0.35258 | 0.35038 | 0.34845 | 0.34676 | 0.34529 | 0.34403 | 0.34296 | 0.34206 | 0.34134 | 0.34076 | 0.34033 | 0.34003 | 0.33985 | 0.33979 | 0.33984 | 0.34 | 0.34024 | 0.34058 | 0.34101 | 0.34152 | 0.3421 | 0.34275 | 0.34347 | 0.34426 | 0.34511 | 0.34602 | 0.34698
6 - Takeoff | 0.17882 | 0.18776 | 0.1967 | 0.20564 | 0.21458 | 0.22352 | 0.23246 | 0.2414 | 0.25034 | 0.25928 | 0.26822 | 0.27717 | 0.28611 | 0.29505 | 0.30399 | 0.31293 | 0.32187 | 0.33081 | 0.33975 | 0.34869 | 0.35763 | 0.36657 | 0.37551 | 0.38446 | 0.3934 | 0.40234 | 0.41128 | 0.42022 | 0.42916 | 0.4381 | 0.44704 | 0.45598 | 0.46492 | 0.47386 | 0.4828 | 0.49175 | 0.50069 | 0.50963 | 0.51857 | 0.52751 | 0.53645
7- Approach | 0 | 0.125 | 0.25 | 0.375 | 0.5
Design Point | 0.405

## Slide 11: Component Estimated Weights and Inertia
Component | Weight Estimate
Wing | 13,560
Empennage | 1406
Nacelles | 9511
Landing Gear | 2316
Power Plant | 4631
Fixed Equipment | 11,660
Empty | 58,350
Weights and inertia estimated from Roskam V supersonic cruise aircraft
  AST-110
  SSXJET
  Super-cruiser
  NAA A3J-1
Ixx (slug-ft2) | Iyy (slug-ft2) | Izz (slug-ft2)
133,600 | 2,357,000 | 1,778,000

## Slide 12: CG Excursion
Mean Aerodynamic Cord (MAC): 26.6 ft
Mean Geometric Cord (MGC): 24.6
At most aft CG,
  Load on NG: 10.67%
  Load on MG: 89.33%
Chart: CG Excursion at Mach 0.95 Cruise
| 74.636116229624392 | 73.373720669915457 | 72.021717408756047 | 77.879161556060822 | 79.130993003101139 | 73.373720669915457
CG Envelope | 58346.0025 | 59726.0025 | 71226.0025 | 129814.9363 | 118314.9363 | 59726.0025
Main Gear Contact | 0 | 129814.9363
Neutral Point | 0 | 129814.9363
Chart: CG Excursion at Mach 2 Cruise
| 74.636116229624392 | 73.373720669915457 | 72.021717408756047 | 77.879161556060822 | 79.130993003101139 | 73.373720669915457
CG Envelope | 58346.0025 | 59726.0025 | 71226.0025 | 129814.9363 | 118314.9363 | 59726.0025
Main Gear Contact | 0 | 129814.9363
Neutral Point | 0 | 129814.9363

## Slide 13: Airfoil Selection
Factors to consider
  Mach cone characteristics
  Design shape (supercritical)
  Thickness effect on Cdwave (function of thickness squared)
 | Tip | Root
Max Thickness | 2% @ 34%c | 3% @ 36%c
Max Camber | 0.5% @ 85%c | 0.6% @ 85%c
http://airfoiltools.com/airfoil/details?airfoil=sc20403-il
http://airfoiltools.com/airfoil/details?airfoil=sc20402-il

## Slide 14: Wing Design
Compound Delta wing configuration
  Aspect Ratio 1.95
  Low aspect ratio requires less extensive internal structure
  Vortex lift at low speeds
  Large fuel storage volume while maintaining low thickness
https://www.heritageconcorde.com

## Slide 15: Wing Design continued
Sweep angles
  Double Delta
  75° and 48°
    High initial sweep to avoid the Mach cone and delay wave drag onset
    Secondary sweep allows for greater area for lift generation and control surfaces
https://history.nasa.gov/SP-60/ch-5.html
X-15 Mach 3.5
X-15 Mach 6

## Slide 16: Drag Polar
Subsonic Drag Polar (Mach .95 cruise conditions)
Supersonic Drag Polar (Mach 2 cruise conditions)
CD,0 (M=0.95)​ | CD,0 (M=2)​ | CD,wave (M=2)​
.00594 | .00619 | .0032​

## Slide 17: V-n Diagram
Selected +3G and -2G as limit loads
  On par with transport category aircraft
Calculated Ve for cruise based on 50,000 ft density (448 fps)
Important speeds
  VA: 481 fps
  Positive load stall: 277 fps
  Negative load stall: 311 fps
Safety factor: 1.5
Example gust: 120 fps
Chart: Equivalent Airspeed (fps)
| 241.28102734392579 | 241.28102734392579
stall_pos | 1 | 0
stall_neg | 0 | -1
connect_stall | 0 | 0
stall_before_va | 1 | 1.25 | 1.546 | 1.9277 | 2.1042 | 2.2491 | 2.5026 | 2.7484 | 3
stall_before_va_neg | -1 | -1.2368 | -1.5422 | -1.6834 | -1.7993 | -2.0021
n_neg | -2 | -2
speed_lim | 3 | -2
gust | 2.9995 | 3.0981 | 3.3079
gust | 3.3079 | 3
connect_1 | 3 | 3
connect_2 | 3 | 3

## Slide 18: Structural Layout and Materials
Materials list:
  Wings, empennage, fuselage: CFRP composites
  Leading edges: titanium
  Nose cone: E-glass reinforced epoxy composite
Structure
  Wings/tail: spars and ribs
  Fuselage: monocoque structure

## Slide 19: Cabin Configuration
1x1 all-business configuration strives balance between comfort and practicality
Seat pitch: 38”
  Average economy: 31”
Seat recline: 8”
  Average economy: 4”
Leg rest
  Raises legs by 30
Seat width: 19” + 2” tray table

## Slide 20: Cabin Configuration, cont’d.
GALLEY
GALLEY
FD
25 rows 1x1 configuration, forward and aft galleys
Four emergency exits (Type C) as per 14 CFR 25.807
Two flight crew, two cabin crew

## Slide 21: Cost Estimate
Chart: Units Produced
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280 | 290 | 300 | 310 | 320 | 330 | 340 | 350 | 360 | 370 | 380 | 390 | 400
 | 886747838.6654 | 525267256.7393 | 394170108.7263 | 324304938.1106 | 280136122.0556 | 249343894.648 | 226468391.052 | 208697853.0007 | 194428166.2767 | 182673285.1658 | 172791579.7008 | 164346346.9354 | 157029343.8559 | 150616352.8483 | 144940096.6631 | 139873055.5528 | 135316190.1517 | 131191321.1235 | 127435847.4785 | 123999003.3765 | 120839152.4653 | 117921797.5051 | 115218092.9219 | 112703717.2883 | 110358007.5457 | 108163286.3514 | 106104333.823 | 104167968.5693 | 102342712.3592 | 100618519.4679 | 98986556.5133 | 97439022.0607 | 95968997.8097 | 94570325.0556 | 93237501.5243 | 91965594.7404 | 90750168.898 | 89587222.8257 | 88473137.1169 | 87404628.8733
Primary goal: estimate cost for 200 production + 3 flight test aircraft
Used relationships from Nicolai & Carichner model
Hourly labor rates varied between $121 and $145 2022 USD
$124 mil unit cost when 200 aircraft produced
  Highly competitive with the market; $30 mil cheaper than Concorde unit cost

## Slide 22: Future Work
Express the CG excursion plot as a function of the % MGC from the LE of MGC
Determine vertical CG spread and landing gear tipover angles
Refine component moment arms
Close CG stability loop
Determine landing gear retraction scheme and precise location, adjusting the engine location as necessary to accommodate
Show pilot line of sight and determine a solution if vision is restricted during takeoff/landing (drooped nose vs camera, etc.)
Determine control surface sizing and placement
Determine stability derivatives
Select engine and inlet that satisfies propulsion requirements

## Slide 23: Questions?